## Slide 1: Interface Editor (using placeholders)
Visualization Interfaces in CODESYS 3 replacing the placeholders of CoDeSys 2.3
Go to Visualization and open the Interface Editor
(In 3s-CODESYS 3 <ALT> <F6>)
Create an SubVisu and define an IN_OUT Variable
VAR_IN_OUT
gves Pointer
VAR_IN
copies the data

## Slide 2: Interface Editor
Create a visu element
and select
theInterface variable
as visualization variable

## Slide 3: Interface Editor
Go to the main visu and call the sub visu as frame
Replace the Reference (Interface variable) with the
variable of your project

## Slide 4: Interface Editor Example
Function Block and Visualization have got the same Data Type as IN/OUT variable.
The same type is declared in the program.
This data type variable is connected to the function block and used as visu reference.

## Slide 5: Visu User Management
Enable the Login Functionality
@ Visualization Manager/ Visualizations
To log in via webvisu the keypad must be enabled.

## Slide 6: Visu User Management
Create User Groups
@ Visualization Manager/ User Management/ Groups

## Slide 7: Visu User Management
Create Users and Passwords
@ Visualization Manager/ User Management/ Users
Usernames and Passwords are key sensitive

## Slide 8: Visu User Management
Create a Log In Button
@ Inputconfiguration

## Slide 9: Visu User Management
Define the element properties
@ Access Rights

## Slide 10: Visualization Manager
Enabling
USE CurrentVisu Variable
synchronizes different visualization clients
The Value of CurrentVisu can be read as:
VisuElems.CURRENTVISU
The pre defined type VisuElems
contains other variables too:

## Slide 11: Visualization Image Pool
Bitmaps are organized in image pools within the project
To add an image pool right click on applicationand add an image pool.

## Slide 12: Visualization Image Pool
In the image pool you can add bitmaps

## Slide 13: Visualization Image Pool
Now you can select the Image from the ImagePool

## Slide 14: Switch Visu Language
Create a Visu Element with Text
Go to the Global Text List
at Project Library
and Add new Languages

## Slide 15: Switch Visu Language
No entry takes over the default text
To generate the language button configure the property „OnMouseDown“

## Slide 16: Switch Visu Language
Select Change the language and select the language to be switched to

## Slide 17: Dynamic Visu Text
Create an element with whatever text
Create a text list with replacements for the boolean values TRUE, FALSE or other data types
Caution: these values are treated as strings

## Slide 18: Dynamic Visu Text
Select the text list with the replacements
Do not forget the …_TO_STRING operator

## Slide 19: Dynamic Bitmaps

## Slide 20: Visu Size
Additional Webvisualizations allow different settings dependeing on the visu client
(Android, IPad, PC….)

## Slide 21: Visu Size
The paint area can be set up at Visualization Properties

## Slide 22: Visu Dialog

## Slide 23: Visu Dialog

## Slide 24: Visu Dialog

## Slide 25: Alarm Table
Add an Alarm configuration to your project
Some default alarm classes will be automatically added

## Slide 26: Alarm Table
You can additionally configure the Alarm class

## Slide 27: Alarm Table
Add an Alarm Group to your Alarm configuration
Add an Alarm Storage to your Alarm configuration

## Slide 28: Visualization Styles
Visualization Styles can be selected and created at the Visualization Manager
To change the style of an existing visualization: generate code close visu and open itagain

## Slide 29: Visualization Styles
Visualization Styles can be selected and created at the Visualization Manager
To change the style of an existing visualization: generate code close visu and open itagain

## Slide 30: Visualization Styles
Derive an new style from an existing style
The Visualization Syles Editor opens
Save the derived style with a different name

## Slide 31: Visualization Styles
Derive an new style from an existing style
Replace the existing pictures with other pictures from your harddrive.

## Slide 32: Visualization Styles
Derive an new style from an existing style
Save and install the file to e!COCKPIT
Close and re-open the Visualization Manager and select the new style
Rocker Switch gray picture has changed