## Slide 1
e!COCKPIT
Fundamentals

## Slide 2: General for controlling the WAGO-I/O-SYSTEM
1
History
IEC 61131
Programming system
Application
Notes: 3
4
5
6
2
1
Contents
General WAGO-I/O-SYSTEM
Hardware
Software
Programming
Data types & variables
Appendix

## Slide 3
Notes: 1
2
3
4
5
6

## Slide 4: History
Programmable Logic Controllers
1965 … 70 In the US, the automotive industry encouraged the development of a new type of control for converting transfer lines
(PLC-Programmable Logic Controllers)
Beginning in 1974 These controllers have been used in Germany as well
(PLC - Programmable Logic Controller)
1983 DIN 19239
1993 DIN IEC 61131-3
Today Large selection of manufacturers. IEC 61131 contains definitions of requirements for modern PLC systems in order to counteract language elements and provide a uniform program structure independent of programming systems.

## Slide 5: IEC 61131-3 − The languages
SFC (Sequential Function Chart)
FBD (Function Block Diagram)
Ladder Logic Diagram (LD)
CFC (Continuous Function Chart)
ST (Structured Text)
IL (Instruction List)
Notes: English |  | German |  | 
abbr. | Designation | abbr. | Designation | Remarks
IL | Instruction List | AWL | Instruction list | Comparable to the assembler
LD | Ladder Diagram | KOP | Ladder diagram | Comparable to a circuit diagram (in exploded view) that has been rotated 90°.
FBD | Function Block Diagram | FBS (FUP) | Function Block- Language | In part (in particular for Siemens STEP 7) also known as LD (Logic Diagram).
SFC | Sequential Function Chart | AS | Sequential function chart | a type of status diagram in STEP 7 known as S7 GRAPH. The IEC 61131-3: 2003 sees the SFC as an evolution of Grafcet according to EN 60848.
ST | Structured Text | ST | Structured text | Derivation of the high level language PASCAL, designated as SCL (Structured Control Language) for STEP 7.
CFC | Continuous Function Chart (Only mentioned in IEC 61131-3) | CFC | Continuous function chart | In CFC, the function blocks (which are identical with those in FBD) are freely positioned.

## Slide 6: Configuration instead of programming
Software libraries
Program: Light_Stairwell
Program: Light_Seminar_2
Notes: There are a number of libraries in different areas, the various components which are already finished.

## Slide 7: Controllers
e!COCKPIT currently supports the following controllers
Programming according to IEC 61131-3
PFC200 750-8202
PFC200 750-8203
PFC200 750-8204
PFC200 750-8206

## Slide 8: PLC cycle
I
O
READ
WRITE
DATA Processing
CYCLE TIME
The time of one PLC cycle depends on the CPU and the length of the program.
Time reaction – PLC cycle
Notes: Like most PLCs, a WAGO controller also functions using the IPO principle. It has an input part, a processing part, and an output part.
The data from connected sensors and actuators are connected to the controller using Input/output devices.
The controller functions cyclically: It reads the values of all the inputs at the beginning of a cycle (“read process image” is also used in conjunction with this).
Afterwards, all program instructions are (sequentially) processed and the assigned outputs are written at the end of the cycle into the output components.
To optimize processing, reading and writing the process data is carried out in one step at the beginning of the cycle.

## Slide 9: Application
Stand alone vs. networked controllers
PLC can control autonomous units
Thanks to the networking features many PLC can be connected to create larger systems
Notes: As a system partner, WAGO solves all automation tasks using centralized and decentralized control architecture in all sectors of industrial, process, and building automation.
The IEC 61131 programming standard is thus an important guideline for modular automation components.
Integrated Web pages and Web-based visualization provide IT applications with real-time process data.
Both large memory and an integrated multitasking system readily meet stringent automation requirements.
A large number of library functions support both software/hardware interfaces and integrated file system.

## Slide 10: Application
Decentralized intelligence with networked controllers