## Slide 1: Appendix
Useful key combinations 6 - 2
Logic functions 6 - 3
Comparisons 6 - 4
Basic calculating options 6 - 5
Standard Function Blocks 6 - 6
Set/ Reset (variants) 6 - 9
Type conversions 6 - 10
Variables and power off 6 - 11
Project structures 6 - 13
Adding libraries 6 - 14
Help sources 6 - 15
Literature 6 - 16
6

## Slide 2
F1 Help
F2 Input help
F5 Start
<Strg>+F7 Write value
F7 Force value
<Strg>+<Umschalt>+F7 Cancel force
<Umschalt>+F2 Variable declaration
<Alt>+F8 Log in
<Strg>+F8 Log out
F4 Next error
Useful key combinations

## Slide 3: Logic functions
AND
OR
XOR
NOT
(or)
(exclusively or)
(not)
(and)
AND
OR
(NAND)
(NOR)
Notes: AND: The output is TRUE, if all inputs are TRUE. (For BOOL, BYTE, WORD, DWORD)
OR: The output is TRUE, if at least one input is TRUE. (For BOOL, BYTE, WORD, DWORD)
XOR: The output is TRUE, it exactly one input is TRUE. (For BOOL, BYTE, WORD, DWORD)
NOT: The output is the opposite of the input. (For BOOL, BYTE, WORD, DWORD)

## Slide 4: Comparisons
GT
GE
LT
LE
(greater equal)
(less than)
(less equal)
(greater than)
EQ
NE
(equal)
(not equal)
Notes: GT: The output is TRUE, if input 1 is greater than input 2. (For all data types)
GE: The output is TRUE, if input 1 is greater than or equal to input 2. (For all data types)
LT: The output is TRUE, if input 1 is less than input 2. (For all data types)
LE: The output is TRUE, if input 1 is less than or equal to input 2. (For all data types)
EQ: The output is TRUE, if both inputs are equal. (For all data types)
NE: The output is TRUE, if both inputs are not equal. (For all data types)

## Slide 5: Basic calculating options
ADD
SUB
MUL
DIV
(add)
(subtract)
(multiply)
(divide)
Notes: ADD: The output is the result of adding the inputs. (For all data types, except BOOL, STRING, DATE, TOD)
SUB: The output is input 1 minus input 2. (For all data types, except BOOL, STRING, DATE, TOD)
MUL: The output is the result of multiplying the inputs. (For all data types, except BOOL, STRING, DATE, TOD)
DIV: The output is input 1 divided by input 2. (For all data types, except BOOL, STRING, DATE, TOD)

## Slide 6: Standard Function Blocks (1)
CLK Q
???
R_TRIG
CLK Q
???
F_TRIG
???
SR
RS – reset/set
(reset has priority)
rising trigger
(recognize rising edge)
falling trigger
(recognize falling edge)
SR – set/reset
(set has priority)
???
RS
SET Q1
RESET1
SET1 Q1
RESET
Notes: SR: A holding element. If the input SET1 were TRUE once, then the output remains TRUE, until the RESET input is TRUE. (only for BOOL)
RS: A holding element. If the input SET1 were TRUE once, then the output remains TRUE, until the RESET input is TRUE. (only for BOOL)
R_TRIG: Reacts to a rising edge of the input CLK and sets the output Q for a program cycle to TRUE. (only for BOOL)
F_TRIG: Reacts to a falling edge of the input CLK and sets the output Q for a program cycle to TRUE. (only for BOOL)

## Slide 7: Standard Function Blocks (2)
???
CTD
???
CTUD
count down
(backward counter)
count up/down
(forward/backward counter)
count up
(forward counter)
???
CTU
CU Q RESET CV
PV
CD Q
LOAD CV
PV
CU QU
CD QD
RESET CV
LOAD
PV
Notes: CTU: At a rising edge at the CU input, the Counter status is increased by 1 at the CV output. If PV is equal to CV, then the output is TRUE. Using the RESET input, the counter can be reset to 0.
CTD: At a rising edge at the LOAD input, CV is equal to PV. At a rising edge at the CD input, the counter status is decreased by 1 at the CV output. The output Q is TRUE if CV equals 0. Output Q becomes TRUE, if CV equals 0.
CTUD: At a rising edge at input LOAD, CV equals PV. At a rising edge at input CD, the counter status on output CV is reduced by 1. At a rising edge on input CU the counter status CV is increased by 1. Using input RESET the counter can be reset to 0. If PV equals CV Output QU becomes TRUE. Output QD becomes TRUE, if CV equals 0.

## Slide 8: Standard Function Blocks (3)
IN Q PT ET
???
TP
IN Q
PT ET
???
TON
IN Q
PT ET
???
TOF
timer on
(timer delay)
timer off
(off delay)
timer pulse
(pulse encoder)
Notes: TP: A rising edge at the Boolean input IN sets the t put Q for the time that is set at the input PT (preset time).
TON: A rising edge at the Boolean input IN starts the Timer and after expiration of the time at input PT, the output Q is TRUE. Output ET is the elapsed time for the timer.
TOF: A rising edge at the Boolean input IN sets the output Q. A falling edge at IN starts the Timer, and after expiration of the time at input PT, Q is again FALSE. Output ET is the elapsed time for the timer. Output ET is the elapsed time for the timer.

## Slide 9: Set/ Reset (variants)
A reset output is set to FALSE, if the associated gate returns TRUE. The output retains its value, even if the gate jumps back to FALSE.
A set output is set to TRUE, if the associated gate returns TRUE. The output retains this value, even if the gate jumps back to FALSE.
GT
LT
temperature
23
temperature
20
heater
R
S
heater

## Slide 10: Type conversions
BOOL
BYTE
DATE
DINT
DT
DWORD
INT
REAL
SINT
STRING
TIME
TOD
UDINT
UDINT
WORD
BOOL
BYTE
DATE
DINT
DT
DWORD
INT
REAL
SINT
STRING
TIME
TOD
UDINT
UDINT
WORD
BOOL_TO_BYTE
BYTE_TO_BOOL
Notes: In general, each data type can be converted into another.
However, data losses can occur in some type conversions.

## Slide 11: Variables and power off
Persistent variables (key word PERSISTENT) maintain their values only after a new download (“online (download)”) as they are not stored in the “retain area”. If persistent variables are also supposed to maintain their previous values following an uncontrolled loss of power, then they must additionally be declared as VAR_RETAIN. Application example: An operating hours counter, which should resume counting following a power failure.
Retain variables (key word RETAIN) keep their values after an uncontrolled termination as well as after normally switching the PLC on or off (according to the “online Reset)” command). Retain variables are, however, re-initialized for “Reset (cold)”, “Reset (original)” and for a new program download. Application example: An item counter in a production line, which continues counting where it left off after a power failure.

## Slide 12: Variables and power off
X = value retained 0 = value is re-initialized
Reset original deletes a program from RAM and Flash memory
 | Reset warm (power off) | Reset cold | Reset original
Standard | 0 | 0 | 0
VAR RETAIN PERSISTENT | X | X | 0

## Slide 13: Project structures
The main program (Subroutines are called from here)
Folder (compilation of modules)
Different Function blocks
A subroutine
Action within a subroutine

## Slide 14: Adding libraries
Using the search box makes it easier to find the correct library

## Slide 15: Help sources
Google.com, Yahoo.com
search for terms like “wago”, “PFC 200”, “e!COCKPIT”
Oscat.de
Open source community for automation technology
Very large, manufacturer independent library with free functions
0571 887 – 555
General support for the WAGO-I/O-SYSTEM
support@wago.com
sps-forum.de
(Knowledge is the only commodity that increases when it is shared)
Many topics about automation, somewhat Simatic-oriented
forum.3s-software.com
The official forum about CODESYS
Threaded topics, often directly for WAGO controllers
Notes: In addition to the substantial teaching offerings by WAGO Kontakttechnik GmbH & Co. KG, there are also numerous online offerings as well as books, which enable further training in a self-directed study in use of the e!COCKPIT software package according to IEC 61131.
In the OSCAT-Forum, examples for the following PLC systems can be found:
Discussions and announcements about the core library, oscat.lib for CODESYS 3.

## Slide 16: Literature
Programming Industrial Automation Systems:
Concepts and Programming Languages, Requirements for Programming Systems, Decision Making Aids, by Karl Heinz John and Michael Tiegelkamp
3rd revised edition 2000 ISBN: 978-3-540-66445-1
PLC Software Development according to IEC 61131. by Jens von Aspern, published May 2000 452 pages, including illustrations and tables, paperback Publisher Hüthig Jehle Rehm GmbH
ISBN: 3778526812
SPS-Programmierung gemäß IEC 61131-3
Mit Beispielen für CODESYS und STEP 7, by Heinrich Lepers (German Language)
2nd edition, dated 05.2007
Franzis Verlag GmbH, ISBN: 3-7723-5805-5
IEC 6113/ Programming
Notes: The book PLC programming according to IEC 61131-3, with examples of CODESYS and STEP 7 by Heinrich Lepers, 4th Edition, of 08.2011, Franzis Verlag GmbH, ISBN: 3 7723-5805-5, is especially highly recommended for migrators from Siemens S7.
Summary (acc. amazon.de)
“The aim of this book is to convince PLC programmers and programming for beginners that programming in higher level languages ​​of the IEC standards (FBS / CFC, ST / SCL and AS / graph) is much more effective, easier to maintain and more cost-efficient than the still widespread programming according to the statement list (STL / LAD / FBD). The book is aimed at both S5 / S7 practitioners who have programmed in STL / LAD / FBD and learn about the benefits of higher IEC-compliant languages ​​CFC, SCL, SFC
and S7-Graph and wish to use it, as well as to all who want to enter as a beginner in programming according to IEC 61131-3. These are trainees in vocational schools, chambers, etc.. and students, but also engineers, technicians, foremen and skilled workers.”